## Slide 1
SLEEP STAGES CLASSIFICATION
USING DEEP LEARNING
supervised by :
DR. Ibrahim Sadek
ENG. Veronica William

## Slide 2
OUR TEAM
WAFAA HASSAN RAMADAN
SOHAILA ELSAYED IBRAHIM
MENNAT ALLAH MOHAMED ELSAYED

## Slide 3
Develop a deep learning–based model for automatic sleep stage classification from physiological signals.
The model analyzes time-series signal data and classifies each segment into one of the five sleep stages:
Wake, N1, N2, N3, and REM.
The proposed system aims to improve the efficiency and accuracy of sleep analysis.
It can assist clinicians by reducing manual scoring effort and increasing the reliability of sleep stage detection.
INTRODUCTION
01

## Slide 4
DATASET
02
The MESA (Multi-Ethnic Study of Atherosclerosis) Sleep Dataset is a large-scale, comprehensive collection of physiological sleep data.
It is hosted by the National Sleep Research Resource (NSRR) and was originally designed to study the links between sleep characteristics and cardiovascular health across a diverse demographic of over 2,000 participants.

## Slide 5
Dataset Structure:
Signal Data (X):
  The input data consists of time-series physiological signals. These signals provide valuable information about brain activity and physiological changes occurring during different sleep stages.
  Each signal sample is represented as a sequence of numerical values describing signal amplitude over time. These signals include measurements of: [EKG, EOG-L, EOG-R, EMG, EEG1, EEG2, EEG3, Pres, Flow, Snore, Thor, Abdo, Leg, Therm, Pos, EKG_Off, EOG-L_Off, EOG-R_Off, EMG_Off, EEG1_Off, EEG2_Off, EEG3_Off, Pleth, OxStatus, SpO2, HR, DHR]
DATASET
03

## Slide 6
annotation (labels) (y)
The XML file acts as a "Time-Stamped Log" or "Metadata Map" created by sleep technicians to describe the continuous signals found in the EDF file.
Sleep Staging :Divides the entire recording into 30-second epochs.
Scored Events (Clinical Observations):Respiratory Events - Oxygen Desaturation - Limb Movements
DATASET
04

## Slide 7
  EOG: Non-invasive electrophysiological technique that records corneo-retinal standing potential
  Captures horizontal and vertical eye movements through potential differences between electrodes
Key Advantages:
  Less invasive than EEG (fewer electrodes)
  Strong correlation with REM sleep (eye movements)
  More suitable for wearable devices
  Lower cost and easier setup
ELECTROOCULOGRAPHY (EOG) SIGNAL
05

## Slide 8
  Develop a robust deep learning framework for multi-class sleep stage classification (Wake, N1, N2, N3, REM) using single-channel EOG
  Transition from conventional multi-channel EEG toward scalable, wearable, and minimally intrusive solutions
  Address inherent class imbalance in sleep stage distribution through advanced sampling and weighting strategies
  Achieve competitive performance (~80% test accuracy) with a computationally lightweight architecture suitable for edge devices
PROJECT OBJECTIVES
06

## Slide 9
  05
  02
Signal Preprocessing
  03
Model
Architecture
  01
Data reading & labeling
  04
Training
pipeline
Evaluation
  06
Preparation
07

## Slide 10
DATA READING
08

## Slide 11
LABELING
09

## Slide 12
SIGNAL PREPROCESSING
10
  Left EOG channel
CHANNEL SELECTION:
FILTERING:
  Band-pass filter (0.3 – 30 Hz) applied to EOG signals.
  Z-score normalization
  Ensures stable training across different participants
NORMALIZATION:
  into 30 seconds to match and align the annotations, given a sampling rate of 256 Hz, each epoch contains 30*256 data points
EPOCHING:

## Slide 13
RAW VS PROCESSED.
11

## Slide 14
RAW VS PROCESSED.
12

## Slide 15
13
DATA PREPARATION & SPLITTING
Signals are divided into 30-second epochs (7680 samples at 256 Hz)
Each epoch is matched with its sleep stage label from the XML file
Invalid epochs or those containing artifacts are discarded
DATA ALIGNMENT:
Sleep stage labels are converted to numerical values: 0 = Wake, 1 = N1, 2 = N2, 3 = N3, 4 = REM
LABEL ENCODING:
The dataset is divided into:
  70% Training
  15% Validation
  15% Test
DATA SPLIT:
HANDLING IMBALANCE:
Sleep stages are highly imbalanced (especially N1 and N3)
Techniques Applied: SMOTE + Class Weights
This improves model performance on minority classes

## Slide 16
-Hybrid Model (CNN + LSTM + Attention)
-Input Single EOG Signal (30 seconds)
-Model Structure:
  Residual CNN Extracts important features from the signal
  Bidirectional LSTM Understands the sequence and timing of sleep patterns
  Attention Mechanism Focuses on the most relevant parts of the signal
  Classification Layer Predicts one of 5 sleep stages:
Wake | N1 | N2 | N3 | REM
Goal: High accuracy with a lightweight model suitable for wearable devices
14
MODEL ARCHITECTURE

## Slide 17
15
MODEL ARCHITECTURE

## Slide 18
We developed 4 versions of the project to improve performance step by step:
MODEL EVOLUTION ACROSS NOTEBOOKS
16

## Slide 19
TRAINING PROCESS & RESULTS
-Training Parameters:
  Epochs: 50
  Batch Size: 32
-Key Observations During Training:
  Training Accuracy reached 99.5% by the final epoch
  Best Validation Accuracy: ~83.2%
  Model shows good convergence with stable training
17

## Slide 20
TRAINING RESULTS
18
1ST VERSION “SIGNALS_EOG1”
2ND VERSION “SIGNALS_EOG2”
3RD VERSION “SIGNALS_EOG3”
4TH VERSION “SIGNALS_EOG4”

## Slide 21
19
TRAINING & VALIDATION CURVES
1ST VERSION “SIGNALS_EOG1”

## Slide 22
20
TRAINING & VALIDATION CURVES
2ND VERSION “SIGNALS_EOG2”

## Slide 23
21
TRAINING & VALIDATION CURVES
3RD VERSION “SIGNALS_EOG3”

## Slide 24
22
TRAINING & VALIDATION CURVES
4TH VERSION “SIGNALS_EOG4”

## Slide 25
EVALUATION & RESULTS
23
1ST VERSION “SIGNALS_EOG1”
2ND VERSION “SIGNALS_EOG2”
3RD VERSION “SIGNALS_EOG3”
4TH VERSION “SIGNALS_EOG4”

## Slide 26
24
CONFUSION MATRICES

## Slide 27
25
1ST VERSION
2ND VERSION
3RD VERSION
4TH VERSION

## Slide 28
26
CLASSFICATION REPORTS

## Slide 29
27
1ST VERSION
2ND VERSION
3RD VERSION
4TH VERSION

## Slide 30
28
ROC CURVES

## Slide 31
29
1ST VERSION
2ND VERSION
3RD VERSION
4TH VERSION

## Slide 32
30
RELATED PAPER
Paper:
U-Sleep: Resilient High-Frequency Sleep Staging
Objective:
Develop a robust deep learning model for automatic sleep stage classification that works with limited channels (EEG + EOG) across different datasets and clinical settings.
Methodology:
  Uses single EEG + single EOG channels
  Fully Convolutional Neural Network (U-Net inspired architecture)
  Trained on large-scale PSG data including MESA dataset
  Works with different sampling rates and electrode placements
  Classify sleep into five stages: Wake, N1, N2, N3, REM
Results:
  High performance on MESA and multiple other datasets
  Mean F1 score around 0.79 across stages (comparable to human experts)
  Strong results with limited channels (EEG + EOG)
  Very resilient and generalizable to new clinical data

## Slide 33
THANK
YOU